## Slide 1: Efficient Synonym Filtering and Scalable Delayed Translation for Hybrid Virtual Caching
Chang Hyun Park, Taekyung Heo, and Jaehyuk Huh
Notes: Good afternoon, welcome to Korea.
Today I’ll be presenting our work “ Efficient Synonym Filtering and Scalable Delayed Translation for Hybrid Virtual Caching”.
This is joint work by myself, Taekyung Huh, and my advisor Professor Jaehyuk Huh

## Slide 2: Physical Caching
Latency constraint limits TLB scalability
  TLB size restricted
  Limited coverage of TLB entry
Missed Opportunities[1]
  Memory access misses TLB, hits in cache
  TLB miss delays cache hit opportunity
L1 $
Last-Level $
TLB
[1] Zhang et al. ICS 2010
Physical Address
Virtual Address
Core
Notes: Current systems that use virtual memory require an address translation from virtual to physical address.
The figure on the left shows the steps that are taken for a memory access, from top to bottom.
The red area highlights components that use virtual addresses, and the blue area components that use physical addresses.
Current systems use physical caching where the cache hierarchy is addressed by physical addresses.
This requires an address translation before accessing the cache, for every memory accesses.
The frequent translation requests and urgency of the memory request for system performance (click) acts as a latency constraint that limits TLB scalability.
The TLB size is restricted due to the latency constraint, and the coverage of current TLB entries are fixed, limiting TLB scalability.
There are also missed opportunities with physically addressed caches.
There are cases where memory accesses that are resident in the cache hierarchy miss in the TLB.
The TLB miss requires a page table walk, even though the data itself is ready in the cache(click), delaying access to the ready cacheline

## Slide 3: Virtual Caching
Delay translation: Virtual Caching
  Access cache, then translate on miss
  Cache hits do not need translation
Problem: Synonyms
  Synonyms are rare[2]
  Optimize for the common case
TLB accesses reduced significantly
  Loosen TLB access latency restriction
  Possibility of sophisticated translation
  Reduces power consumption
L1 $
Last-Level $
TLB
Physical Address
Virtual Address
Core
Last-Level $
Synonyms
L1 $
[2] Basu et al. ISCA 2012
Notes: Virtual caching was proposed long ago, and provides the benefit of accessing the virtual cache without a translation.
The translation is delayed to after a cache miss.
However, despite the benefits virtual cache suffers synonym problems . (Click)
Synonyms are problematic because two or more virtual addresses can be mapped to a single physical address.
With only virtual addresses, it is difficult to find the other virtual cacheline sharing the same block. This makes maintaining coherence difficult.
In this work, we exploit the fact that synonyms are sparingly used. This was an observation made by a prior work
Finally, Delaying translation to after LLC misses reduces TLB accesses significantly.
This allows us to loosen the restrictions imposed on current TLBs, and explore more sophisticated translations, and also reduces power consumed by the TLB.

## Slide 4: Hybrid Virtual Caching
L1 $
Last-Level $
TLB
Physical Address
Virtual Address
Core
Synonyms
Virtual Caching
L1 $
Last-Level $
TLB
Physical Address
Virtual Address
Core
Physical Caching
Physical Address
Virtual Address
Hybrid Virtual Caching
L1 $
Last-Level $
$
Core
Delayed TLB
Scalable Delayed Translation
Notes: In this work, we propose hybrid virtual caching, a hybrid of both physical and virtual caching.
Common accesses use the virtual cache, and synonyms requiring special attention use the physical cache.
By doing so, we can defer translation of the majority of memory accesses to after a LLC miss.
Furthermore,
(click) By exploiting the delayed TLB access reductions, we propose a scalable delayed translation, that extends on segment based translation proposed by prior work that improves translation scalability..

## Slide 5: Contributions
Propose hybrid virtual physical caching
  Cache populated by both virtual and physical blocks
  Virtual cache for common case, physical for synonyms
  Synonyms not confined to fixed address range, use entire cache
Propose scalable yet flexible delayed translation
  Improve TLB entry scalability by employing segments [2][3]
  Provide many segments for flexibility of memory management
  Propose efficient search mechanism to lookup segment
[2] Basu et al. ISCA 2013
[3] Karakostas, Gandhi et al. ISCA 2015
Notes: Our contributions are as follows:
We propose a hybrid virtual cache where the cache is populated by both virtual and physically addressed cachelines.
We optimize for the common case.
Distinctions from prior work is that the synonym pages are not restricted to a fixed address range,
And the entire cache hierarchy, multiple levels, use hybrid virtual caching.
We identify that even with delayed translation current TLBs mapping fixed granularity translations are not scalable.
We extend on prior work that advocated the use of segments, and propose a scalable many segment translation system that provides scalability and flexibility for the memory management system.
For today’s talk, I’ll talk about hybrid virtual caching first, and then scalable delayed translation.

## Slide 6: Hybrid Virtual Caching
Virtual and physical cache
  Each page consistently determined as physical or virtual
  Cache tags hold either tags
  Challenge: Choose address before cache access
Synonym Filter: Bloom Filter that detects synonyms
  HW managed by OS
  Synonyms always detected, translated to physical address
L1 $
Last-Level $
$
Delayed TLB
Non-Synonyms
Synonyms
Core
Notes: Hybrid virtual cache functions as a virtual and physical cache.
Each cacheline is populated as either physical or virtual, and all accesses to the cachelines are consistently decided as physical or virtual.
The challenge of this approach is that the address to be used for cache access, either virtual or physical address, must be decided prior to accessing the cache hierarchy.
(click)
We introduce a synonym filter, that quickly and consistently determines an access to use either virtual or physical address.
We use Bloom Filter for this job.
The synonym filter is a hardware managed by the OS, where the OS adds synonym pages to the bloom filter, and swaps filter context on context switches.
By design, the bloom filter may produce false positives, but false negatives are never produced.
In other words, synonym pages are always detected.
The filter may additionally detect non-synonym pages as Synonyms, however such cases are very rare, less than 1% of accesses, and our system is designed to withstand false positives. The details are in the paper.
I’ll show you a quick illustration of the translation steps of hybrid virtual caching
(click) We place the synonym filter between the core and the cache hierarchy. A memory request leaving the core must first filtered by the synonym filter.
(click) The majority of accesses are to non-synonyms, and so the virtual address is used to access the cache.
A hit in the cache hierarchy does not require any further address translation, reducing translations.
If the non synonym causes a last level cache miss, (click), the request goes through a delayed translation to get the physical address and accesses the memory.
(click) For rare accesses that are to synonym pages, the synonym filter will detect these requests and
(click) Translate the address from virtual to physical using a small TLB.
(click)The memory request will access the cache using physical address preventing synonyms from creating cache incoherency.
On a last level cache miss, the request accesses the memory without having to translate the address.

## Slide 7: Hybrid Virtual Caching Efficiency
Pin-based simulation
Baseline TLB
  L1 TLB: 64 entries
  L2 TLB: 1024 entries
Hybrid Virtual Caching
  2x1Kb Synonym filters
  Synonym TLB: 64 entries
  Delayed TLB: 1024 entries
Workloads
  Apache, Ferret, Firefox, Postgres, SpecJBB
Physical Address
Virtual Address
Hybrid Virtual Caching
L1 $
Last-Level $
$
Core
Delayed TLB
Notes: To measure the efficiency of hybrid virtual caching we built a pin-based simulator.
The baseline TLB is modeled after the Intel Haswell mico-architecture, and
For the hybrid virtual caching, we implemented the synonym filter using two one kilobit filters.
We used a small TLB for the rare synonym translations, and a larger TLB for the common delayed translation.

## Slide 8: Hybrid Virtual Caching Efficiency
Physical Address
Virtual Address
Hybrid Virtual Caching
L1 $
Last-Level $
$
Core
Delayed TLB
83.7~99.9% TLB accesses bypassed
Synonym Filter
Up to 99.9% TLB access reduction
Up to 69.7% TLB miss reduction
Delayed Translation
Majority of accesses to virtual cache
Cache hits remove TLB accesses and reduce TLB misses
Notes: We found that the synonym filter allowed 83 to 99% of accesses to access the cache before a translation.
Furthermore, our hybrid virtual cache reduced delayed TLB accesses by up to 99% and delayed TLB misses by up to 69%
(click)Hybrid virtual caching allows accessing the cache without a translation for majority of accesses.
(click)A cache hit ends a memory request preventing delayed translation, therefore the accesses to the delayed TLB and misses are reduced significantly by cache hits.

## Slide 9: Limitation of Delayed TLB
TLB entries limited in scalability
  Each entry maps fixed granularity
  Increasing TLB size does not reduce miss as expected
Chart: Norm. TLB MPKI (%)
| tigr | Mcf | Milc | GUPS
1K Entries | 100 | 100 | 100 | 100
2K | 97.8274 | 95.7326 | 99.9944 | 99.9197
4K | 93.6988 | 93.1731 | 99.5555 | 99.7952
8K | 83.2928 | 89.1142 | 90.5776 | 99.5718
16K | 55.6484 | 83.6671 | 90.0184 | 99.1366
32K | 36.3362 | 76.4931 | 89.6665 | 98.2812
64K | 19.6562 | 67.5381 | 85.1803 | 96.5994
TLB size is restricted,
Improve coverage of TLB entry
Notes: However, delaying translation in itself isn’t a solution to limited TLB scalability.
Even with delayed translation, some workloads still suffer from severe TLB misses.
The reason is because current Fixed granularity TLBs, or TLBs that map fixed page sizes, are limited in scalability.
We find that increasing the number of TLB entries does not result in sufficient TLB miss reduction.
We conducted a scalability test of the TLB on a delayed translation system. (click)
We show the result of benchmarks with severe TLB misses even after benefiting from delayed translation.
We continuously increased the number of TLB entries from 1K entries on the far left, through 64K entries on the right.
The plotted bars show the TLB misses normalized to the configuration with 1K entries.
The graph shows that larger TLBs do offer some TLB miss reduction, however, the scalability of current TLBs are limited.
(click) As increasing the size of the TLB does not result in expected improvements, we turn to improving coverage of the TLB entries.

## Slide 10: Segments: Scalable Translation
Direct Segment[2] improves TLB entry coverage
  Represented by three values (base, limit, offset)
  Translates contiguous memory of any size
OS benefits from more available segments
  Memory sharing among processes fragment memory
  OS can offer multiple smaller segments
Number of segments[3] limited by latency
  Segment lookup between Core and L1 cache
  Fully-associative lookup of all segments required
[2] Basu et al. ISCA 2013
[3] Karakostas, Gandhi et al. ISCA 2015
Virtual Address Space
Base
Limit
Physical Address Space
Offset
Notes: To improve the coverage offered by each TLB entry, we employ segments, that was proposed by a prior work.
Segments represents a contiguous memory mapping of any size, using three register values, base limit and offset.
(click) Segments require contiguous pages to function, however the memory availability depends on the memory usage of the system and other processes executing on the system.
The OS can benefit from more segments, as large memory allocation requests of processes can be satisfied with numerous smaller segments
(click)In prior work, the segments are placed between the Core and L1 cache, imposing strict latency requirements.
This restricts the size and complexity of the segment lookup, limiting the number of segments.
One thing to note is that for any incoming virtual address, all segments need to be looked up in a fully-associative manner, to check if the virtual address belongs to the segment.

## Slide 11: Scalable Delayed Translation
Exploit reduced frequency of delayed translation
  Prior work limited to 10s of segments
  Provide 1000s of segments for OS Flexibility
Efficient searching of owner segment required
  OS managed tree that locates segment in a HW table
  HW walker that traverses tree to acquire location
  Use location (index) to access segment in HW table
32 Segments
1000s Segments
Delay Translation
Notes: Prior work was limited to 32 segments, because of the latency restrictions.
We exploit the benefit of hybrid virtual caching, where the number of delayed translation requests are significantly reduced.
We provide thousands of segments to support OS with memory management flexibility.
With many segments, locating the owning segment of an incoming virtual address becomes increasingly important.
It is infeasible to lookup thousands of segments with a fully-associative lookup.
Thus we propose an efficient searching mechanism where for a given virtual address, a location or index to the segment table is returned.
Using the index, the segment is directly accessed in the segment table.
We explain the searching mechanism in the slides to follow.

## Slide 12: Scalable Delayed Translation
LLC Miss (Non-synonym)
Memory Access
Index Tree
Segment index
Index | Base | Limit | Offset | etc.
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
… |  |  |  | 
Segment Table
Segment Table: register values for many segments
Index Tree: B-tree that holds following mapping
  key: virtual address
  value: index to Segment Table
Infeasible to search all Segment Table entries
Notes: First off the translation information is held in the segment table.
One of the segments in the table owns an incoming virtual address, and translates it to physical address.
However, the table holds thousands of segments, and the incoming virtual address needs to find the owner segment.
A naïve approach would be a fully associative lookup. (click) However such lookup is prohibitive due to the size of the table.
(click) Therefore we keep an Index tree, which is a B-tree that maps an incoming virtual address to an index pointing to the owning segment in the segment table.
After traversing the tree (click) the segment index is produced, and using the index the owning segment is located allowing the virtual address to be translated to physical address.

## Slide 13: Scalable Delayed Translation
LLC Miss (Non-synonym)
Memory Access
Index Tree
Traverse tree
Index Cache
Segment index
Index | Base | Limit | Offset | etc.
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
… |  |  |  | 
Segment Table
HW Walker
Index Cache: caches index tree nodes on-chip
Hardware Walker: searches through the index tree to produce a segment table index
Notes: However, accesses to off-chip memory take too long, and so an (click) Index Cache is added to cache the index tree.
The (click) multiple node tree traversal is conducted in the index cache, and a (click) hardware walker does the actual traversing.
So we speed up the looking up of the segment index by adding the index cache.

## Slide 14: Address Translation Procedure
LLC Miss (Non-synonym)
Memory Access
Segment Cache
Hit
Segment index
Index | Base | Limit | Offset | etc.
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
… |  |  |  | 
Segment Table
Miss
Index Tree
Traverse tree
Index Cache
HW Walker
Segment Cache: caches many segment translation
Reduces latency and power consumption
Notes: Finally, index caches require multiple lookups, as there are up to multiple levels of the tree, (four in our configuration), and so it is beneficial to cache the many-segment translation.
We use a TLB like fixed granularity translation table to cache the translation results.
(click)The segment cache helps reduce translation latency and reduce power consumption.

## Slide 15: Evaluation
Full system OoO simulation on Marssx86 + DRAMSim2
  Hosts Linux with 4GB RAM (DDR3)
Three level cache hierarchy (based on Intel CPUs)
Baseline TLB configurations (based on Intel Haswell)
  L1 TLB: 1 cycle, 64 entry, 4-way
  L2 TLB: 7 cycle, 1024 entry, 8-way
Delayed TLB configurations range 1K - 16K entry
Many segment translation configurations
  Segment Table: 2K entries
  Index Cache: 32KB
  Segment Cache: 128 entry
Benchmarks: SPECCPU, NPB, biobench, gups
Notes: We evaluated the proposed hybrid virtual caching and scalable delayed translation on a Marssx86, a full-system simulator.
The Baseline TLB configurations were based on the Intel Haswell microarchitecture.
All results will be normalized to this baseline.
We evaluated the performance of delayed fixed granularity TLBs, that we denote ‘delayed TLB’ that range in size form 1K to 16K.
The configurations of our scalable delayed translation, which we denote as many segment translation is shown below.
For reference, the area overhead of the many segment translation is slightly larger than a fixed granularity TLB of 8K entries.

## Slide 16: Results
Chart: Normalized IPC to Baseline TLB (%)
| bzip2 | DC | gamess | perlbench | cactusADM | astar | LU | gromacs
Delayed TLB 1K entries | 104.712 | 104.8712 | 105.4174 | 106.45 | 107.7867 | 107.3888 | 107.7917 | 109.2924
4K | 104.7335 | 104.8727 | 105.3853 | 107.1554 | 107.8706 | 107.9495 | 107.8266 | 109.6625
16K | 104.7678 | 104.8686 | 105.4424 | 107.6794 | 108.0655 | 108.5173 | 107.8476 | 109.6403
Many Segment Translation | 104.8286 | 104.8741 | 105.486 | 107.8018 | 108.4749 | 108.5763 | 108.0339 | 109.8555
Cache hits reduce TLB accesses & misses Improving Performance
Notes: The graphs show the normalized IPC of each configuration normalized to the execution of the baseline system.
Each bar represents different configurations, where the first three show delayed fixed granularity translation of TLBs,
each having different number of entries.
Finally the red bar shows the result of many segment translation.
First we present the results of workloads that benefit from delayed translation.
These workloads benefit directly from delayed translation where cache hits reduce TLB accesses and misses(click).
The workloads show little or no performance improvement with larger TLBs and many segment translations.

## Slide 17: Results
Chart: Normalized IPC to Baseline TLB (%)
| milc | CG | gcc | sjeng | xalancbmk | hmmer | soplex | mcf | omnetpp | sphinx3 | gups | tigr | Geomean
Delayed TLB 1K entries | 88.8458 | 99.9007 | 100.8914 | 99.7488 | 93.6577 | 100.8749 | 98.1332 | 91.5841 | 92.1953 | 101.5021 | 95.6433 | 91.2559 | 100.201
4K | 88.813 | 99.8417 | 101.3022 | 99.7146 | 95.6629 | 101.0221 | 101.0831 | 91.7156 | 92.8109 | 101.5576 | 95.6413 | 91.0513 | 100.5905
16K | 88.8138 | 100.1852 | 103.08 | 100.3629 | 103.2401 | 103.0254 | 104.6962 | 92.4659 | 102.6531 | 110.3624 | 95.6445 | 113.034 | 103.5474
Many Segment Translation | 101.7582 | 102.1137 | 103.2277 | 103.4079 | 103.4888 | 104.1578 | 104.7616 | 107.3503 | 112.4343 | 112.5463 | 143.2199 | 179.36 | 110.7002
Delayed TLB is not scalable for these workloads
Delayed TLB offers some scalability
143
179
Scalable Delayed Translation improves performance by 10.7% on average
Power consumption is reduced by 60% on average
Increased translation scalability significantly reduces TLB misses
Notes: The second set of benchmarks show the results for workloads that show the limitation of the TLBs mapping fixed page sizes.
We show the results of fixed granularity delayed TLB first.
(click) Some workloads show little improvement in performance with the increase of TLB size.
(click) Other workloads show slight performance improvement with increased TLB size.
(click) With scalable delayed translation, we can improve the performance by improving the scalability of translation performance.
(click) Scalable delayed translation provides 10.7% performance improvement, and (click) reduction of 60& power consumption of translation components.

## Slide 18: Conclusion
Hybrid Virtual Cache allows delaying address translation
  Majority of memory accesses use virtual caching, synonyms use physical caching
  Synonym Filter consistently and quickly identifies access to synonym pages
  Reduces up to 99.9% of TLB accesses, 69.7% of TLB misses
Scalable delayed translation
  Exploits reduced translations
  Provides many segments and efficient segment searching
  Average 10.7% performance improvement, 60% power saving
Notes: In conclusion,
We propose hybrid virtual cache that delays translation for the common case, and takes special care for the problematic synonym pages.
Our synonym filter provides consistent and quick identification of synonym pages.
(Hybrid virtual caching significantly reduces delayed TLB accesses and misses)
Hybrid virtual caching allows 99.9% of accesses to virtual cache without translation
It can also reduce up to 69.7% of delayed translation, due to cache hits.
Furthermore for workloads that suffer due to the restrictions of the TLB, scalable delayed translation improves the scalbility of translation.
Our evaluation shows that both hybrid virtual caching and scalable delayed translation provides an average of 10.7% performance improvement and 60% power saving of the address translation components for the chosen workloads.

## Slide 19: Thank You
Notes: Thank you for your time, I’ll take questions.

## Slide 20: Related Work
Work focused on improving TLB scalability
  Direct Segments, RMM, CoLT, Clustered TLB
  Tried to solve TLB issue within latency and complexity restrictions imposed by physical caching
Work that benefit from Delayed Translation
  Enigma: made use of additional address space in PowerPC architecture
  Virtual Memory w/o TLBs: proposes software cache miss handler
Work that propose using Virtual Caches
  OVC: primary focus was on power reduction
  Efficient virtual-cache coherence: self-invalidating protocols

## Slide 21: More in the Paper
Extension of Cache Tag arrays
Handling False positives of synonym filters
Permission handling
Handling changes in memory mappings and permissions
Management of the synonym filter by the OS
Sensitivity study of size of index cache
Virtualization for hybrid virtual cache and scalable delayed translation
Power consumption evaluation